## Slide 1: TOKSIKOLOGI PELARUT
Departemen K3
FKM Universitas Indonesia
2020
Prof. Dra. Fatma Lestari, M.Si., PhD.

## Slide 2: TOPIK PEMBAHASAN
Sifat-Sifat Pelarut Organik
Faktor Risiko
Identifikasi Toksikan & Jalur Pajanan
Definisi Pelarut Organik
Dosis
Biotransformasi & Eliminasi
Contoh Pelarut Organik di Tempat Kerja
Distribusi, Toksisitas Lokal and Sistemik
Hubungan Dosis-Respons

## Slide 3
Definisi Pelarut
Pelarut: Zat yang dapat melarutkan zat lainnya (terlarut - solute) membentuk larutan yang terdispersi secara uniform (larutan - solution) pada level ion maupun molecular (Smith, P., 2008)
Pelarut air (water based)
Pelarut organic (solvent based)
Pelarut

## Slide 4
Mengapa Pelarut Digunakan di Industri?
Keuntungan Pelarut Organik
Harga murah
Banyak tersedia
Karakteristik beragam: mudah larut dalam air (methanol, etanol)…ada yang mudah larut dalam larutan organik (n-heksana, n-pentana)
Mudah menguap

## Slide 5
Cleaning
Degreasing
Thinning
Extraction
Penggunaan Pelarut di Industri
Etanol
Isopropanol
Toluene
Xylene
Solvent mixtures e.g. white spirits
Metanol
Heksana
Penggunaan
Jenis Pelarut Organik

## Slide 6
Penggunaan Pelarut di Industri
Sumber: Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Organic Solvents
Agrochemicals, pharmaceuticals and fine chemicals (65-70% of tonnage); man made fiber (20-25%)
Ethanol: It is used in perfumes, cosmetics, paints, detergents and inks. Ethanol has antiseptic & disinfectant properties it slows or stops the growth of micro-organisms (germs).
paint thinner, contact cement & model airplane glue.

## Slide 7
Penggunaan Pelarut di Industri
Sumber: Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Organic Solvents
Cyclohexane goes into the production of intermediates for nylon, which has a variety of common applications such as clothing, tents and carpets as well as thermoplastics.
Cyclohexane is also used as a solvent in chemical and industrial processes and recently has been substituted for benzene in many applications.
Glycol ethers are found in pharmaceuticals, sunscreens, cosmetics, inks, dyes & water-based paints (E-series), they are also used in degreasers, cleaners, aerosol paints and adhesives (P-series)

## Slide 8
Sumber gambar: Google image.
Sumber: Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Organic Solvents
Penggunaan Pelarut di Industri

## Slide 9
Sifat-sifat Pelarut Organik
Kelarutan
Mudah terbakar (Flammable) & Mudah Meledak (Eksplosif)
Kemudahan menguap (Volatility)
Larut dalam air (polar)
Etanol, methanol, glycol
Tidak Larut dalam air (non-polar)
N-heksana, sikloheksana, toluen
Mudah terbakar
Methanol (dipakai dalam campuran bahan bakar)
Tidak Mudah terbakar
Glycol (antifreeze)
Mudah menguap
Toluen, Xylene (dipakai untuk pelarut cat)
Tidak Mudah menguap
Glycol (antifreeze)

## Slide 10
Menentukan efisiensi sebagai pelarut
Menentukan efek kesehatan
Sebagian besar pelarut organik mudah larut dalam lemak
Potensi sebagai Pelarut, anestetik, penghilang lemak solvents (de-fatting agents) – berhubungan dengan kemudahan larut dalam lemak
  Sifat Pelarut Organik:
  Kelarutan dalam Lemak

## Slide 11
Methanol: LEL: 6%; UEL:36% (kisaran: 30%) - lebar
Carbon disulphide LEL: 1.0%, UEL = 50% (kisaran 49%) - lebar
Benzene LEL: 1,2%; LEL:7,8% (kisaran 6,2%) - sempit
  Sifat Pelarut Organik:
  Kemudahan terbakar & meledak
Kemudahan terbakar – Flammability
Flash point < 23°C – sangat mudah terbakar
Flash point 23°- 61°C
kemudahan terbakar sedang
Flash point > 61°C – tidak mudah terbakar
Kemudahan meledak – Explosiveness
Explosive limits
Makin lebar kisaran LEL & UEL, makin besar bahaya kebakaran
Flashpoint
Upper explosive limit (UEL) is the highest concentration of solvent in air that will ignite.
Lower explosive limit (LEL) is the lowest concentration of solvent in air that will ignite.
> UEL Terlalu kaya
< LEL terlalu miskin (too lean)

## Slide 12
Kemudahan menguap (Volatility)
  Makin mudah menguap – makin besar konsentrasi uapnya diudara
Sebagian besar pelarut organik mudah menguap (volatile)
  benzene, toluene, methylene chloride, methyl chloroform  glues, solvents, varnishes, adhesives and paints
  Sifat Pelarut Organik:
  Kemudahan menguap (Volatility)
Inhalation = main route of exposure
Highly dependent on volatility
Vapour Pressure
Makin tinggi Vapour Pressure – makin mudah menguap
Low Vapour Pressure
High Vapour Pressure
Titik didih
Makin rendah titik didih– makin mudah menguap
Titik didih Tinggi
Titik didih Rendah

## Slide 13
Volatile Organic Compounds (VOCs)
Organic chemical compounds whose composition makes it possible for them to evaporate under normal indoor atmospheric conditions of temperature and pressure (EPA, 2014)
Examples
  Benzene
  Ethylene glycol
  Formaldehyde
  Methylene chloride
  Tetrachloroethylene
  Toluene
  Xylene
  Sifat Pelarut Organik:
  Kemudahan menguap (Volatility)

## Slide 14
Sifat fisik pelarut organik

## Slide 15
Solvents are divided into families according to chemical structure and attached functional groups
Toxic properties tend to be similar within a group, e.g. liver toxicity from chlorinated hydrocarbons, irritation from aldehydes
Basic structure
Aliphatic
Alicyclic
Aromatic
Functional groups
Halogens
Alcohols
Ketones
Glycols
Esters
Ethers
Carboxylic acids
Amines
Amides
  Sifat Pelarut Organik
  Struktur Kimiawi

## Slide 16
  Families of Organic Compounds
  Sifat Pelarut Organik
  Struktur Kimiawi
Notes: Aromatic Chemicals
Include at least one benzene ring.
Aromatics are far more irritating than aliphatics

## Slide 17: Faktor Risiko Pelarut Organik

## Slide 18: Faktor Risiko Pelarut Organik di Tempat Kerja
Millions of workers are exposed to solvents on a daily basis.
Health hazards associated with solvent exposure include toxicity to the nervous system, reproductive damage, liver and kidney damage, respiratory impairment, cancer & dermatitis. (OSHA)

## Slide 19: Identifikasi Toksikan
Bahan kimia apa yang terkandung didalamnya?
Safety data sheet (SDS)
Campuran, nama dagang “Solvent 100” - Cat Kapal Laut
Analisis Komposisi Gas Chromatography  Ethylbenzene, propyl benzene
Komposisi tidak diketahui  Analisis: Electron impact Gas Chromatography Mass Spectrometry (EI-GC-MS)
Notes: The toxicologist must understand several variables when dealing with the effect of any xenobiotic compound on human health. The first fundamental question that must be and answered in dealing with a chemical exposure by both toxicologist and industrial hygienist is what is chmeical

## Slide 20: Jalur Pajanan
Pajanan terjadi:
Maintenance work – pipa dibuka, pompa dan valve diangkat untuk diservis
Fugitive emissions kebocoran pada valves and joints.
Spillages
Transfer of solvents – pajanan dapat terjadi pada saat transfer pelarut dari vessels, tanks atau drums.
Produksi pelarut organik umumnya TERTUTUP (ENCLOSED)

## Slide 21: Jalur Pajanan
Inhalasi
Absorpsi kulit
Tertelan
Absorpsi mata
Rute utama

## Slide 22: Jalur Pajanan Faktor-faktor yang memengaruhi pajanan pelarut
Konsentrasi uap
Konsentrasi makin tinggi pada ruang terbatas & tertutup (confined space)
Frekuensi pajanan
Kemudahan menguap
Kelarutan
mudah larut dalam lemak makin mudah masuk ke dalam tubuh

## Slide 23: Jalur Pajanan Inhalasi
Jalur utama pajanan pelarut di tempat kerja
Uptake (% dosis terhirup, tertahan & terabsorpsi): 40-80% at rest
Peningkatan aktivitas fisik – ↑ absorpsi
Uap – masuk ke paru-paru – ke darah
Luas permukaan paru-paru - 140 m2 - Lapisan tipis sel mudah ditembus alveoli – pertukaran gas O2 & CO2 darah
Luas permukaan kulit: 1.5 - 2 m2

## Slide 24: Jalur Pajanan - Inhalasi

## Slide 25: Jalur Pajanan – Absorpsi Kulit
Kelarutan dalam lemak
Pelarut mudah larut dalam lemak & air - ↑ penetrasi
Skin absorption rates – bervariasi antar individu (max 4 kali)
Faktor-faktor memengaruhi penetrasi pelarut kedalam kulit:
  Ketebalan kulit
  Kerusakan kulit (terluka, abrasi)
  Difusi pasif (polar / non-polar) – mekanisme beda
  Kondisi kulit (kering) ↑ penetrasi
https://toxtutor.nlm.nih.gov/10-004.html

## Slide 26: Dosis
Dosis ≠ konsentrasi
Dosis terabsorpsi: jumlah toksikan masuk melewati membran ke dalam sistem kompartemen biologis
Variabel yang memengaruhi:
  Jalur pajanan
  Target organ
  Konsentrasi pajanan
  Distribusi
  Metabolisme
All substances are poisons; there is none which is not a poison. The right dose differentiates a poison from a remedy.” Paracelcus

## Slide 27: Distribusi & Toksisitas Lokal & Systemik
Distribusi dipengaruhi:
  Fugacity: flux or movement tendency of a compound in a multiphase system
  Kelarutan dalam lemak
  Perfusi
  Laju aliran darah
Kow: Konstanta untuk kelarutan dalam lemak
Senyawa Kow tinggi – mudah larut dalam jaringan lemak tubuh – umumnya mudah dieliminasi
Lokal & systemic effects bergantung dari konsentari toksikan & metabolitnya
Lokal  perubahan terjadi pada lokasi kontak pajanan
Sistemik  perubahan terjadi pada beberapa titik jauh dari kontak pajanan
partition coefficient

## Slide 28: Hubungan Dosis Response
Respons: gangguan/perubahan fisiologis dari kondisi normal
Respons:
  All or none response (discrete)
  Graded response. E.g. blood pressure increase
Response of organic solvents
  Lokal: Erythema, blistering & burn effect (local). Methylene chloride  severe irritation
  Graded response (systemic); dizzines, lightheadedness, sensory disturbance, nausea, narcosis
Benzene  leukemia dan atherosclerosis (CS2), axonal neuropathy (n-hexane dan methyl-n-butyl ketone)

## Slide 29: Efek Kesehatan - Umum
Efek Akut
Sakit kepala
Mengantuk
Mual
Pusing
Kulit terkelupas
Tidak sadarkan diri
Kematian
Efek Kronik
Dermatitis
Kerusakan hati
Kerusakan ginjal
Memengaruhi fungsi otak & system syaraf pusat: mudah marah, gangguan tidur, dimensia
Memengaruhi sistem reproduksi & janin

## Slide 30
Biotransformasi & Eliminasi
Distribution
  Masuk ke dalam jaringan lemak
  Jarisan adiposa (including nervous system and liver), organs with large blood flow (cardiac, skeletal muscle).
  Most solvents cross placenta & enter breast milk
Metabolism
  Some metabolised extensively and some not at all
  For some solvents, metabolism plays a role in their toxicity
Excretion
  Primarily through exhalation of unchanged compound, metabolites in urine or combination of both
  Eg Perchloroethylene is poorly metabolized and excreted primarily to exhalation
  Biological half life can vary from a few minutes to a few days

## Slide 31: Toksisitas Pelarut Organik di Tempat Kerja

## Slide 32
Pelarut organik di tempat kerja
Alkanes
Formaldehyde
Benzene
Toluene
Styrene
Tetrachloroethylene (perchloroethylene)
Methylene Chloride
2-Butanone (methyl ethyl ketone)

## Slide 33
Toksisitas Pelarut – Efek toksik sekelompok Pelarut
Sumber: Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Organic Solvents

## Slide 34
Compounds are gases, liquids and solids
  Gases e.g. Methane, ethane, propane, butane (odorless)
  Liquids e.g. pentane, hexane, heptane octane
  Solids e.g. paraffin wax
Explosion Hazard
  E.g. Flixborough, England
Generally low toxicity
  Methane, ethane, propane = simple asphyxiants
  Hexane and heptane most commonly used general purpose solvents
Cause anesthesia, respiratory tract irritation, dermatitis, neurobehavioural dysfunction
Flixborough Accident: https://www.youtube.com/watch?v=8A1xSCUtB-M
Pelarut organik di tempat kerja
Alkana

## Slide 35
Toksisitas Pelarut – Kelompok Alifatik
Sumber: Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Organic Solvents

## Slide 36
Pelarut organik di tempat kerja
Alkohol
Alkohol yang umum digunakan: Methanol, Ethanol, n-propanol, isopropanol, n-hexanol, glycerine - bau menyengat
Penggunaan:
    Cleaning agents, thinners, diluents, chemical intermediates, in paint/ pharmaceutical / pesticide manufacture
    Low melting points result in some alcohols being used as a anti-freeze agent.
    Sebagian alkohol: flammable or combustible
    Toxicokinetics
      50% of inhaled alcohol is absorbed at rest
      Some alcohols may be absorbed through the skin

## Slide 37
Pelarut organik di tempat kerja
Alkohol
Efek Kesehatan
CNS Depressants
  All alcohols cause narcosis
  Acute symptoms from overexposure range from fatigue, in-coordination, and behavioural changes to coma.
  Irritants
    Irritating to the mucous membranes
    Eye/respiratory tract irritation usually occur at lower concentrations than CNS depression—useful warning property

## Slide 38
Karakteristik: Tidak berwarna, jernih, mudah terbakar, berbau manis, Sangat mudah menguap
Penggunaan
  Terdapat dalam campuran BBM
  Pelarut adesif & penghilang cat
  Industri sepatu & karet
  Bahan awal dalam sintesis plastik
  Sangat ketat diatur – 1-5% kandungan benzene dalam BBM
  Terdapat dalam asap rokok
Pelarut organik di tempat kerja
Benzena

## Slide 39
Efek Kesehatan
inhalasi & absorpsi kulit
Efek Akut
  nervous system -- headache, tiredness, nausea, dizziness, narcosis & loss of consciousness
  Affects nervous system – behavioural & psychomotor changes occur
  High exposure levels can cause death by CNS depression or cardiac arrhythmia
  Skin exposure causes dermatitis, and inhalation of high concentrations may result in bronchial irritation or pulmonary oedema
Pelarut organik di tempat kerja
Benzena
Efek Kronik
  Depression of bone marrow
  Meningkatkan risiko anemia aplastil
  Pekerja pajanan kronik benzene – sel darah merah jumlahnya 50% dari normal.
  Now rare as exposures are well controlled
IARC Classification – carcinogenic to humans Leukaemia

## Slide 40
Toksisitas Pelarut – Kelompok Aromatik
Sumber: Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Organic Solvents

## Slide 41
Toksisitas Pelarut – Kelompok Pelarut Terhalogenasi
Sumber: Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Organic Solvents

## Slide 42
Toksisitas Pelarut – Efek terhadap Reproduksi
Sumber: Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Organic Solvents

## Slide 43: REFERENCES
Smith, P.A (2008). Toxicology of Organic Solvents Chapter 16 –Toxicology Principles for the Industrial Hygienist
LaDou, J. (2007). Current Occupational and Environmental Medicine. Chapter 29 - Solvents
Winder C & Stacey N., (2005) Occupational Toxicology. 2nd Edition. Taylor and Francis (615.902) Chapter 11 –Toxicity of Solvents
Dick, F. (2006). Solvent Neurotoxicity. Occupational & Environmental Medicine, 63, 221-226.