## Slide 1
Risk Management and Bow Tie 1 (Sesi 13)
DR.dr.Zulkifli Djunaidi, MAppSc 02/10/2020

## Slide 2
Managing Safety and Health Risk - Objectives
The hazards inherent in the operations have been
systematically identified and assessed and are fully
understood at the appropriate levels in the organisation
01
03
02
Arrangements are in place to control these hazards and to deal with the consequences should the need arise
The necessary information, training, auditing and improvement process are in place
To ensure that:

## Slide 3
HSE Risk and Bow Tie
Definition
Risk = Consequence resulting from the release of a hazard
x
Probability of the occurrence of that event

## Slide 4
Identify
Are people exposed to harm resulting from the
company’s operations?
Assess
What are the causes, consequences & effects?
How likely is the loss of control?
What is the risk & is it ALARP?
Control
Can the causes be eliminated?
What controls are needed & can they be effective?
Recover
Can the potential consequences & effects be mitigated?
What are the recovery measures required?
Are the recovery capabilities suitable & sufficient?
Effects of Safety and Health Hazards

## Slide 5
Step 1 - Hazard
Identify all Hazard

## Slide 6
HAZARD - Definition
Definition
Anything that has the potential to cause harm, ill health
and injury, damage to property, products or the
environment, production losses or increase liabilities
Hazard
At workplace categorized:
Physical, Chemical, Biological & Physcosocial

## Slide 7
Hazard - examples
Chemical
Hydrocarbon under pressure
Smoke
Toxic material
Volatile fluids in tanks
Physical
Moving road tankers / vehicles
Elevated objects
Noise
People working at heights
High voltage
Biological
Toxicological lab
(catering facility at distant work station)
Physicosocial
Working outside the country without family members.

## Slide 8
Step 2 – Top Event

## Slide 9
“
List Top Events or Incidents which will
result when hazards are released and
relate them to the hazards identified
Step 2 - Top Event

## Slide 10
“
Step 2 - Top Event
Top Event is defined as:
The incident which occurs as a result of the hazard
being released
Hazard
Top Event
(Incident)

## Slide 11
Top Event - examples
Loss of containment
Electrical shock
Fall from heights
Exposure to toxic material
Exposure to radioactive material
Effluent discharge into waterways
Emissions of toxic gases

## Slide 12
Step 3 - Consequences
List consequences which result from hazard being released

## Slide 13
“
Consequence –
definition
Consequence is defined as:
An event or chain of events that results from the hazard being released
Hazard
Top Event
(Incident)
Asset
Damage
People
Environment
Reputation

## Slide 14
Consequences - examples
Serious injury
Death
Latent illness or disease which has long gestation period
Property damage - own or public
Environmental damage
Loss of reputation leading to loss in current and
prospective business
Loss of revenue - paying for compensation, medical expenses, production loss or deferment

## Slide 15
Step 4 - Hazard register

## Slide 16
Compile a Hazards & Effects register listing Hazards,
Top Event & Consequences
Hazard
Threats
Barriers
Top
Event
Recovery
Measures
P
A
E
R
Initial
Risk
Final
Risk
Risk
Rating
Remedial
Action
Required
HAZARDS & EFFECTS REGISTER
X
X
X
X
X
X
X
X
X
X
X
X
Consequences
Step 4 - Hazard register

## Slide 17
Step 5 -Risk ranking
Using the Risk Matrix & brainstorming techniques rank the hazards and consequences based on the probabilities of the Top Event occurring

## Slide 18
RISK MATRIX

## Slide 19
Ranking Risk Probability
Hazard
Threats
Barriers
Top
Event
Recovery
Measures
P
A
E
R
Initial
Risk
Final
Risk
Risk
Rating
Remedial
Action
Required
HAZARDS & EFFECTS REGISTER
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Consequences
X
X
X
X

## Slide 20
Harm to people
Consequence - definition

## Slide 21
Consequence - definition
Damage to Asset

## Slide 22
Consequence - definition
Effect on the Environment

## Slide 23
Consequence - definition
Impact on Reputation

## Slide 24
Step 6 - Threats
For all hazards and consequences which have been ranked as HIGH risks, identify all threats or causes which can release the hazard to become a top event

## Slide 25
“
Threat - definition
Threat is defined as:
A possible cause that will release the hazard to become a top event-includes thermal, biological, electrical, chemical, kinetic, climatic, radiation or human factors
Hazard
Top Event
(Incident)
Asset
Damage
People
Environment
Reputation
Threat
Threat
Threat

## Slide 26
Threat - examples
High temperature
Corrosion
Bacteria
Overpressure
Erosion
High voltage
Ultraviolet radiation
Environmental conditions
Human incompetence
Design / process unknowns

## Slide 27
Step 7 - Barriers
Determine Barriers for each threat

## Slide 28
“
Barrier - definition
A barrier is defined as:
A measure which is put in to prevent the release of a hazard or to prevent the occurrence of a top event once the hazard is released - barriers may be physical or non- physical
Hazard
Top Event
(Incident)
Asset
Damage
People
Environment
Reputation
Threat
Threat
Threat
Barrier
Barrier
Barrier
Barrier
Barrier
Barrier

## Slide 29
Barrier - examples
Guards or protective shields e.g. protective coatings,
corrosion inhibitors, machine guards, fencing etc.
Pressure / safety relief valves
High temperature cut-off switches
Correct / valid operating procedures
Time delays in processes
Lowering speeds of equipment
Carrying maintenance when it is due
Reducing congestion in operating areas

## Slide 30
Step 8 - Recovery Measures
Determine the Recovery Measures to reduce the
impact of the Consequences due to the occurrence
of the Top Event

## Slide 31
Recovery Measures
H
A
Z
A
R
D
T
H
R
E
A
T
B
A
R
R
I
E
R
TOP
EVENT
C
O
N
T
A
I
N
M
E
N
T
M
I
T
I
G
A
T
I
O
N
R
E
S
T
O
R
A
T
I
O
N
P
A
E
R
Activity or Condition which causes
hazard release
Proactive
control
Incident
Recovery Measures
Consequences

## Slide 32
Recovery Measures - examples
Gas, fire & smoke alarms
Emergency Shutdown systems
Firewater deluge systems
Fire and blast walls
Emergency Response plans, training & drills
Business Resumption Plans

## Slide 33
Step 9 - Escalation factors
Identify Escalation Factors which will reduce the
effectiveness or operation of the barriers or
recovery measures and implement additional
measures to compensate for these factors

## Slide 34
“
Escalation factors –
definition
Escalation factors is defined as:
Conditions that lead to increased risk due to loss of barriers or loss of recovery measures especially life saving or mitigating capabilities
Hazard
Top Event
(Incident)
Asset
Damage
People
Environment
Reputation
Threat
Threat
Threat
Barrier
Barrier
Barrier
Barrier
Barrier
Barrier
Recovery
Measures
Recovery
Measures
Recovery
Measures
Recovery
Measures
Escalation
controls

## Slide 35
Escalation Controls - examples
Abnormal operating condition e.g critical standby
equipment is under maintenance during an emergency
Plant operating outside the design envelope
Extreme environmental conditions - may not allow
the activation of planned recovery measures
Incorrect operation of the plant due to unavailability
of updated operating procedures
Human error due to lack of competence or ineffective
training

## Slide 36
Use the ALARP principle to
test whether the controls
are sufficient

## Slide 37
AS LOW AS REASONABLY PRACTICABLE

## Slide 38
Step 10
Complete the Hazard Analysis
and the Hazards & Effects Register

## Slide 39
Full hazard analysis
Hazard
Top Event
(Incident)
Asset
Damage
People
Environment
Reputation
Threat
Threat
Threat
Barrier
Barrier
Barrier
Barrier
Barrier
Barrier
Recovery
Measures
Recovery
Measures
Recovery
Measures
Recovery
Measures
Escalation
controls
Proactive Controls
Reactive Controls

## Slide 40
Hazard
Threats
Barriers
Top
Event
Recovery
Measures
P
A
E
R
Initial
Risk
Final
Risk
Risk
Rating
Remedial
Action
Required
HAZARDS & EFFECTS REGISTER
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
C5
D4,5
E3,4,5
X
X
Consequences
X
X
X
C5
D4,5
E3,4,5
X
X
X
X
X
X
X
X
X
Completed Hazards & Effects Register

## Slide 41
Step 11
Link Barriers and Recovery Measure
controls to HSE Critical Activities
which are part of Business Activities

## Slide 42
HSE Critical Activities
HSE Critical Activities are the activities that require
to be carried out to ensure the effectiveness and
correct operation of the Barriers and Recovery Measures
at all times
These activities are broken down into tasks
For all these tasks, standards have to be specified and clear & valid procedures should be available
Competency requirements for the staff to carry out the
task and also for the supervisors should be made clear.
Where there are gaps, they should be sent for training

## Slide 43
Step 12

## Slide 44
Step 12
Control
Recovery
Measures
Top
Event
Consequences
Hazard
Barrier
Standards
Procedures
Inputs
HSE
critical
task
HSE
Critical activity
Business Activity
Design & Construction
Operations
Maintenance
Inspection
Staff
Supervisor
Competency
Reports
Performance
Measures
Outputs

## Slide 45
Activity
Hydrocarbon liquid under
pressure in tanks
Task
Barrier
Threat
Hazard
External corrosion
External coating of
tanks
Maintain tanks
Execute maintenance
Input
Maint. procedures
Maint. Strategy
Failure record
Output
Tank repair
report
Performance criteria
Trend on corrosion of
tank
Responsible party
Competence
Maint. Mgr.
Technician
Example on Barrier
10 yrs maint exp.
3 yrs operations exp.
5 yrs experience
Tech. training
Activity – Hazard relationship

## Slide 46
Activity
Hydrocarbon liquid under
pressure in tanks
Task
Recovery
Measure
Consequence
Hazard
Oil spill
Emergency Response
plan
ERP drill
HSE support activity
Input
Govt. Regulations
ERP/Oil spill response
plan
Output
Emergency
Drill report
Performance criteria
Trend in emergency response
Responsible party
Competence
HSE Mgr.
HSE Technician
Example on
Recovery Measure
Exp. Firefighting
& oil spill response
Competent to
Operate response
equipment
51
Activity – Hazard relationship

## Slide 47
Examples Of Identifying & Managing Safety and Health Risk
Next few slides….
Identify
Assess
Control
Recovery

## Slide 48
Hazard
Threat
Barrier
Top
Event
Recovery
Measures
Consequences
Moving
Vehicle
Slippery
Road
Slow Down
Loss of
Control
ABS
Accident,
Injuries,
Fatalities
Examples Of Identifying & Managing Safety and Health Risk

## Slide 49
Diesel
(unloading into skid tank)
Refined hydrocarbon
Threat 1
Threat 2
Threat 3
Threat 4
Threat n
Incompetent driver
Not sure discharge procedure
Poor attitude
Barriers
Training
Supervision
Design of skid tank
Escalation factors (saboteur)
Multiple supplier non standard fittings
Top Event
Loss of containment
Recovery
Preparedness
Measures
Bundwall valve open
Consequence 3
Consequence 2
Consequence 1
Consequence n
Spill/contamination
Stop work order
Company’s reputation
C
O
N
S
E
Q
U
E
N
C
E
S
ER procedure
Bund-wall
Supervision

## Slide 50
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 51: The Children & the Bull
Hazard = the bull
Top Event = Loss of containment (escape of bull)
Threats Controls/Barriers Escalation Factors
  corroded fence – galvanised material – acid rain
  rotting posts – treated wood – termites, age – metal posts – corrosion
  bull leans on fence – barbed wire – anger (state of mind) – Red Ball, barking dog
  bull charges fence – barbed wire, 4 strands – yelling child, dog – metal posts – electric fence
  falling tree limbs – prune trees – weather, age, insects
  gate unlatched/open – sign, lock – ability to read, – vandalism

## Slide 52: The Children & the Bull
Consequences = multiple fatalites
Top Event = Loss of containment (escape of bull)
Recovery Measures Esalation. Factors Escalation Factor Controls
dog attack bull
dog not trained
send for regular training
run to car
panic situation
carry out simulation exercise
shoot the bull
failed to fire
Regular service of gun
climb tree
Height phobia
Therapy and practice
run in different
directions
panic situation
carry out simulation exercise

## Slide 53
Coincident or Not ?
If,
A B C D E F G H I J K L M N O P Q R S T U V W X Y Z
Equals,
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26
Then,
K + N + O + W + L + E + D + G + E
11 + 14 + 15 + 23 + 12 + 5 + 4 + 7 + 5 = 96%
H + A + R + D + W + O + R + K
8 + 1 + 18 + 4 + 23 + 15 + 18 + 11 = 98%
Both are important, but the total falls just short of 100%
But,
A + T + T + I + T + U + D + E
1 + 20 + 20 + 9 + 20 + 21 + 4 + 5 = 100%
Safety really is about attitude. Make 100% Safe Behavior your choice
both ON and OFF the job

## Slide 54
THANK YOU