## Slide 1
RISK ASSESSMENT TABLES
DR.dr. Zulkifli Djunaidi, MAppSc
Sesi 8
16/10/2020

## Slide 2
RISK ASSESSMENT METHODS
Qualitative
Semi Quantitative
Quantitative

## Slide 6: RISK ASSESSMENT PROCESS

## Slide 7
Model Analisis Risiko
Matriks (Qualitative)
  Probabilitas/Matematik (Quantitative)
Index/Scoring
(Semi Quantitative)
Terdapat 3 (tiga) tipe model yang sering digunakan, yaitu (Engberg, 2008):

## Slide 8
Perbedaan | Matriks | Index/Scoring | Probabilitas/ Matematik
Pengertian | Model sederhana berbentuk matriks yang membuat ranking risiko berdasarkan nilai probabilitas dan konsekuensi dari suatu kejadian ataupun proses. Variabel Probabilitas dan Konsekuensi diberi ranking seperti tinggi (high), sedang (medium) dan rendah (low) atau dalam ranking angka seperti 1,2,3,4,5 | Model berbentuk index yang merupakan kumpulan penilaian (scoring) terhadap faktor-faktor yang mempengaruhi variabel probabilitas dan konsekuensi. Setiap faktor yang berpengaruh terhadap risiko diberi bobot dalam kisaran nilai minimum dan maximum score sesuai dengan kriteria yang merujuk kepada standar dan peraturan yang berlaku. | Model berbentuk formula matematik yang lebih kompleks dan berdasarkan analisis risiko secara kuantitatif (Quantitative Risk Assessment Model) terhadap data-data kejadian kegagalan diwaktu yang lalu. Perhitungan biasanya dilakukan dengan matematik ataupun statistik
Perbedaan Model Matriks, Index/Scoring dan Probabilitas

## Slide 9
Metode | Kualitatif Risiko kemudian ditentukan sebagai koordinat nilai probabilitas dan konsekuensi | Semi Kuantitatif Hasil risiko yang didapat bersifat relatif (relative risk) | Kuantitatif menggunakan statistik atau Event/Fault Tree Analysis. Hasil yang didapat bersifat absolut (absolute risk).
Keterbatasan | Akurasi dianggap lemah jika tidak berdasarkan data-data kuantitatif | Penilaian seringkali dinilai terlalu subyektif karena dilakukan secara profesional judgment bila data tidak tersedia. | Biaya tinggi dan membutuhkan waktu yang lebih lama karena analisis dilakukan pada setiap faktor yang mempengaruhi variabel probabilitas dan konsekuensi Seringkali mengalami kesulitan bila data-data tidak lengkap
Perbedaan | Matriks | Index/Scoring | Probabilitas/ Matematik

## Slide 10
Keunggulan | Biaya rendah, dan cepat memberikan gambaran umum mengenai level risiko yang ada sehingga dapat dijadikan sebagai masukan pada proses pengambilan keputusan. Oleh karena iu model ini juga disebut sebagai decision making analysis model. | Biaya rendah, dan cepat memberikan gambaran umum mengenai level risiko dan lokasi-lokasi berisiko yang ada disepanjang jalur pipa. Komperhensif dan terpadu karena menggunakan data-data kuantitatif terhadap seluruh faktor yang mempengaruhi risiko. | Lebih akurat
Perbedaan | Matriks | Index/Scoring | Probabilitas/ Matematik
. Sumber: Engberg, D. J. Johns Hopkins University, Baltimore, MD, 2008

## Slide 11: Tabel Konsekuensi Analisa Risiko Semi Kuantitatif (Kriteria Risiko Fine)

## Slide 12: Consequences Table

## Slide 13: Tabel Exposure Analisa Risiko Semi Kuantitatif (Kriteria Risiko Fine)
Exposure | Continously | Sering terjadi dalam sehari | 10
Frekuensi pemajanan terhadap bahaya | Frequently | 1 kali dalam sehari | 6
 | Occasionally | 1 kali seminggu sampai 1 kali sebulan | 3
 | Infrequent | 1 kali dalam sebulan sampai 1 kali dalam setahun | 2
 | Rare | Pernah terjadi pada waktu yang lama di masa lalu | 1
 | Very Rare | Tidak pernah terjadi di masa lalu | 0,5

## Slide 14: Tabel Probability Analisa Risiko Semi Kuantitatif (Kriteria Risiko Fine)
Probability | Almost certain | Hampir sering terjadi | 10
Kemungkinan yang menyertai suatu akibat | Likely | kemungkinan terjadinya 50%-50% | 6
 | Unusual but possible | tidak biasa namun mungkin terjadi | 3
 | Remotely possible | kecil kemungkinan terjadi | 1
 | Conceivable | Tidak pernah terjadi sebelumnya, tetapi mungkin terjadi di masa mendatang | 0,5
 | Practically Imposible | Tidak mungkin terjadi | 0,1
Sumber : AS/NZS 4360 :2004

## Slide 15: Level/Prioritas Risiko (Fine Chart)
Tingkat Risiko | Comment | Action
> 350 | Very High | Penghentian aktifitas sampai risiko dikurangi
180 – 350 | Priority 1 | Penanganan secepatnya
70 – 180 | Subtancial | Mengharuskan ada perbaikan
20 – 70 | Priority 3 | Memerlukan perhatian
< 20 | Acceptable | Lakukan kegiatan sesuai SOP
Sumber : AS/NZS 4360 :2004

## Slide 17
Fault-Tree Analysis
This is a method of constructing a sequence of events that will lead to a failure or undesired event. The event must be characterised by three parameters, what, where and when – e.g. explosion in the main boiler room during shutdown.
The method then tracks back to trace the faults and failures that are needed for this event to take place.
METODE

## Slide 18
Contoh FTA

## Slide 19
Each of the three contributing events in the circles would then be analysed to determine how they arise, by extending the fault tree backwards.
Control measures for the critical events in the fault tree could then be devised.
In this particular instance it would be by controlling both the ignition and gas release.
The line for air would not normally be extended back, since in normal circumstances air will be present.
Explanation of FTA example

## Slide 20
In failure mode effects analysis the effect of the failure of each component part of the system is considered, whether it is to fail to safety or to danger.
In industrial situations this method would calculate the probability of failure to give a composite failure rate for the whole system.
This method is quite good for deciding what spares to keep.
Failure Mode Effects Analysis (FMEA)

## Slide 21: Example for a hydraulic pump: (FMEA Case)

## Slide 22
HAZOP and HAZAN (Hazard Analysis) were developed by ICI and are widely used in process industries.
The basis of the method is to study the effect of deviations on the system (without initially establishing how those deviations have been created)
Hazard And Operability Studies (HAZOP)

## Slide 23
Hazops Case
(example)
For instance if a pipe is to carry helium gas, then the method would consider what if:
  The helium flow rate is too high
  The helium flow rate is too low
  The helium is moving in the wrong direction
  It is carrying something other than helium
  It is carrying something in addition to helium
  It is carrying nothing at all
  The helium is too hot
  The helium is too cold.
  The pressure is too high
  The pressure is too low
If any of these were predicted to produce a particularly catastrophic outcome, then consideration would be given to the circumstances in which it might happen, in order to produce a control strategy.

## Slide 24: Worked example (Hazops)
In this example, chemical A is mixed with chemical B to produce C. Too much or too little of A or B will result in inadequate reaction and the production of an undesirable toxic product instead of C.

## Slide 25
Hazops
Analysis

## Slide 26
Selection of The Risk Techniques
When the need is to. | Technique to use
Study specific events. perform post-incident investigations, compare risks of specific failures. calculate specific event probabilities | Event trees. fault trees, FMEA. PRA, HAZOP
Obtain an inexpensive overall risk model, create a resource allocation model, model the interaction of many potential failure mechanisms, study or create an operating discipline | Indexing model
Better quantify a belief, create a simple decision support tool, combine several beliefs into a single solution, document choices in resource allocation | Matrix model

## Slide 27
RISK LEVEL
Basic Level
(without considering the existing program)
Existing level
(By considering the existing program)
Predictive Level
(By considering recommended program)

## Slide 28
Thank You