## Slide 1: MK Bioengineering Bioinstrumentation & Biosensors For Tissue Engineering
Prasandhya Astagiri Yusuf, S.Si., M.T., Ph.D.
Department of Medical Physics
Faculty of Medicine Universitas Indonesia

## Slide 2
Table of Contents
Biosensors
1
2
4
5
3
6
Bioreceptors
Biotransducer
Immunosensors
Bioreactors
Organs on Chips

## Slide 3
Biosensors - Introduction
Biosensor
A self-contained analytical device that combines a biological component with a physicochemical component for the detection or quantification of an analyte of biological importance
Biological (blood, urine, saliva)
Enviromental (water, air, soil)
Bioreceptor (nucleic acid, cells, antibody, enzyme)
Electrical Interface (nanowire array, nanoparticles, electrode)
Signal Amplifier
Signal Processor
Display
Bioreceptor
Detector
Transducer
Output
Receptor
Transducer
Electric
Signal
Molecule

## Slide 4: Bioreceptors / Biosensing Components
Receptor
Transducer
Electric
Signal
Molecule
Catalytic Type
  Enzymes
  Microbes
  Organelles
  Cells or Tissues
Affinity Type
  Antibodies
  Receptors
  Nucleic Acids
Electrochemical
Optical
Magnetic
Acoustic
Calorimetric
Piezoelectric

## Slide 5: Biotransducer in Immunosensor
Kubicek-Sutherland et al 2017 Biosensors

## Slide 6: Enzymatic Biosensors
Enzymes are catalysts for biochemical reactions; large macromolecules consisting mostly of protein, and usually containing a prosthetic group (metals)
Usually proteins of oxidase type that can selectively react with specific analytes, consume dissolved O2 , and produce H2 O2 that is an easily detectable compound
Substrate: the target molecule of an enzymatic reaction
S + E ES E+P
  S: substrate; E: enzyme;
  ES: enzyme-substrate complex;
  P: product
Reaction rate vs. substrate concentration at constant enzyme concentration

## Slide 7: Immunosensors
Immunosensors: based on highly specific antigen-antibody reactions
Detection of the reaction (binding/association) can be either direct or indirect (labeled)
ELISA: Competitive & Sandwich ELISA
Antigen-binding sites
Light chain
Heavy chain
Hinge region
Fc region
Fab region

## Slide 8: Tissue Engineering Bioreactors
Mixing Bioreactors
Tissue engineering bioreactors are in vitro cell culture systems that have been designed to alter the following basic physiological phenomena: cell survival along with tissue structure, organization, and function
They can deliver both a productive three-dimensional culture environment and instructive stimuli
Also known as dynamic culture bioreactors, supplying nutrients and removing waste by consistently circulating the media, whether through stirring, rocking, or perfusion
 Allow for convection instead of relying on diffusion in static cell culture
Blose et al. 2013
Spinner flask
Perfusion through a construct
Perfusion across
the surface of a construct
Rocker platform

## Slide 9: Cell Seeding Bioreactors
A secondary function of bioreactors is to distribute cells optimally throughout a scaffold prior to long-term culture
Vacuums, electromagnetism, and acoustic waves force cells to distribute throughout the thickness of scaffolds
Rotation can be used to help achieve a more uniform circumferential distribution and overcome the effects of settling from gravity
Blose et al. 2013

## Slide 10: Guiding Tissue Structure and Function
Chemical stimulation
  Represents a large variety of bioactive factors including growth factors, hormones, and chemical additives, which are added to the cell culture media to induce effects, such as proliferation or differentiation.
Mechanical stimulation
  Though many complex loading patterns can exist within the body, most loading patterns used in bioreactors can be described simply through some combination of following:
Shear
Pressure
Compression
Stretch
Torsion
Bending

## Slide 11: Organs On Chips